## Slide 1: Salsa User Manual last update February 2020

## Slide 2: Index
Software architecture...........6
COMETE graphical library...9
Software packages............10 Salsa lexicon......................11
Salsa description...............12
Salsa User Manual 2

## Slide 3: Description index
Environment variables......................................................................12
Preferences settings.........................................................................13
  Scan server device settings
  Data fitter device settings
  Historic log settings
  Data recording settings
  Enable confirmation settings
  Scan server device properties settings
  Nexus file browser integration
Salsa mode.......................................................................................14
  Configuration mode
  Configuration manager
  Salsa read only
  Salsa result
Salsa User Manual 3

## Slide 4: Functionalities index
Create a new configuration...............................................................18
General parameters..........................19
  Number of scan
  Actuators delay
  Zig zag trajectory
  Scan on the fly
  Scan speed adjustment
  After run function and scan function
Scan parameters..............................20
  Sensors
  Time bases
  Actuators
  Trajectories
  Hooks
  Error strategies
Scan execution............23
  Start
  Abort
  Pause
  Resume
Salsa User Manual 4

## Slide 5: Functionalities index
Scan result.........................................................................................24
  Display manager
  1D scan result
  2D scan result
  Scan functions
  Error strategies
  Scan historic
  Salsa logging
Other functionalities...........................................................................31
  Perspectives
  Data fitter
  Data recorder
  Bookmarks
  Search tool
  Custom trajectory
Salsa User Manual 5
  Open Nexus files
  Get trajectory from scan image

## Slide 6: Software architecture
Salsa User Manual 6
ds_ScanServer
actuators, sensors, trajectory
data_01,data_02…
Hooks, ScanFunctions
Start,Abort,Pause,Resume
ds_DataRecorder
NeXus files
ds_DataFitter
fittedDataArray
Python
SalsaAPI
ds_SimpleScan
Passerelle acteur V3
startRecording
Fit data_01
SalsaDB
Configurations
Start Configuration

## Slide 7: Software architecture
Salsa User Manual 7
ds_ScanServer
actuators, sensors, trajectory
data_01,data_02…
Hooks, ScanFunctions
Start,Abort,Pause,Resume
ds_DataRecorder
NeXus files
ds_DataFitter
fittedDataArray
COMETE Graphical library
CurrentScanResultBean
DataFitterBean
DataRecorderBean

## Slide 8: Software architecture
Salsa User Manual 8
SalsaAPI
SalsaDB
Configurations

## Slide 9: COMETE graphical library
Salsa User Manual 9
TANGO
NEXUS
Archivage
Librairie ATK
COMETE graphical library

## Slide 10: Software packages
Salsa User Manual 10
DEVICE_ROOT
ds_ScanServer
ds_DataRecorder
ds_DataFitter
LIVE_ROOT
SALSA
PASSERELLE_ROOT
Passerelle
Bossanova
SalsaAPI
Comete
SalsaAPI (Duplication)
DataRecorderBean
DataFitterBean
ScanResultBean

## Slide 11: Salsa lexicon
Salsa User Manual 11
TANGO : The control system of SOLEIL
Device : A TANGO programm for remoting a equipement or processing.
Attribute : An equipment or a process parameter (eg : position or integration time).
Command : An equipment or a process action (eg : Move or Count)
Scan server device : The Tango device server for processing scan.
Nexus : Format of files of SOLEIL.
Sensor : listened Tango parameter
Actuator : moved Tango parameter
Hook : A simple Tango command (no argument as Start, Close…)
Perspective : A custom view disposition.

## Slide 12: Environment variables
Salsa User Manual 12
Salsa needs for several environment variables to be set.
TANGO_HOST
Host of the tango database (localhost:20001)
SALSA_SERVER_URL
Url of the salsa database (jdbc:mysql://localhost/salsa)
  SALSA_LOGIN
  The login of the user connected on Salsa database
  SALSA_PERSPECTIVES_DIRECTORY
  The folder for the perspectives files
  SALSA_DEVICE_PREFERENCES
  The file for the device configurations
  SALSA_UI_PREFERENCES
  The file for the user interface configurations

## Slide 13: Salsa Preferences settings
Salsa User Manual 13
  Log file setting
  Scan server device setting
  Data Fitter device setting
  Nexus file browser application

## Slide 14: Salsa Mode
Salsa User Manual 14
Configuration mode : (“salsa” command)
In this mode you can create, modify and remove a scan configuration.
All the configuration edition views are available in the Menu
Window > Show View > Configuration Views

## Slide 15: Salsa Mode
Salsa User Manual 15
Configuration manager
The management of several configurations is possible now.
You can Add, Remove, Enable/Disable a TimeBase, Sensor or Actuator on several configurations.
Select several configuration in the Scan Manager Tree.
The devices appear in red color, are the uncommon devices.

## Slide 16: Salsa Mode
Salsa User Manual 16
Salsa read only: (“salsa-ro” command)
In this mode you can only select a Scan configuration from the bookmark, modify the scan configuration (delete or add devices, or hook is not possible).
And you can play the configuration.

## Slide 17: Salsa Mode
Salsa User Manual 17
Salsa result : (“salsa-result” command)
In this mode you can only visualize the current scan result.
All the views for the visualization are available in the Menu :
Window > Show View > Result Views

## Slide 18: Create a new configuration
Salsa User Manual 18
New scan configuration. Several kinds of scan exist
1D = dimension X
2D = dimension X et dimension Y
HCS = 1D continu hardware with a time base
K = 1D specific trajectory in 3 phases
E = 1D trajectory visualed differently in a table
Click on the New button
Or right click on the tree to make appears the configuration management menu.

## Slide 19: General parameters
Salsa User Manual 19
  LINE/EX/SCAN.1/scanNumber
  LINE/EX/SCAN.1/ actuatorsDelay
  LINE/EX/SCAN.1/ zigzag
  LINE/EX/SCAN.1/ onTheFly
  LINE/EX/SCAN.1/ enableScanSpeed
  LINE/EX/SCAN.1/ afterRunActionType
scanserver attributes

## Slide 20: Scan parameters
Salsa User Manual 20
  LINE/EX/SCAN.1/sensors
  LINE/EX/SCAN.1/timebases
  LINE/EX/SCAN.1/actuators
  LINE/EX/SCAN.1/trajectories
  Predefined values defined in the device properties :
    ActuatorsFile,
    SensorsFile,
    TimebasesFile
scanserver attributes

## Slide 21: Hooks configuration
Salsa User Manual 21
  LINE/EX/SCAN.1/postActuatorMoveHooks
  LINE/EX/SCAN.1/postIntegrationHooks
  LINE/EX/SCAN.1/postRunHooks
  LINE/EX/SCAN.1/postScanHooks
  LINE/EX/SCAN.1/postStepHooks
  …
scanserver attributes

## Slide 22: Error strategy
Salsa User Manual 22
  LINE/EX/SCAN.1/sensorsErrorStrategy
  LINE/EX/SCAN.1/sensorsRetryCount
  LINE/EX/SCAN.1/contextValidation
scanserver attributes

## Slide 23: Scan execution
First select a configuration before starting a scan configuration.
When no configuration is selected, the Start button is disabled.
Salsa User Manual 23
Start button.
Scan server command:
LINE/EX/SCAN.1/Start
Pause button.
Scan server command:
LINE/EX/SCAN.1/Pause
Resume button.
Scan server command:
LINE/EX/SCAN.1/Resume
Abort button.
Scan server command:
LINE/EX/SCAN.1/Abort

## Slide 24: Display manager
  LINE/EX/SCAN.1/actuatorsDataList
  LINE/EX/SCAN.1/sensorsDataList
  LINE/EX/SCAN.1/sensorsTimestamps
  LINE/EX/SCAN.1/actuatorsTimestamps
  LINE/EX/FIT.1/fittedDataY
Salsa User Manual 24
scanserver attributes
datafitter attributes

## Slide 25: 1D scan result visualization
Salsa User Manual 25
  LINE/EX/SCAN.1/data_XX scanserver attribute
  Send the actuator to the selected point.
Click on a point

## Slide 26: 2D scan result visualization
Salsa User Manual 26
  LINE/EX/SCAN.1/data_XX scanserver attribute
  Send the actuator to the selected point.

## Slide 27: 2D scan as N spectra
Salsa User Manual 27
Display a 2D Image as N Spectra in Chart
  LINE/EX/SCAN.1/data_XX scanserver attribute

## Slide 28: Scan functions
Salsa User Manual 28
Executed by the user on demand (except in Abort case) !
  LINE/EX/SCAN.1/afterRunActionType
  LINE/EX/SCAN.1/afterRunActionSensor
  LINE/EX/SCAN.1/afterRunActionActuator
  LINE/EX/SCAN.1/afterRunActionActuatorValue
  Commande LINE/EX/SCAN.1/ExecuteAction
scanserver attributes

## Slide 29: Scan historic
Salsa User Manual 29
Current scan historic (can be very useful for debugging !)
  LINE/EX/SCAN.1/historic scanserver attribute

## Slide 30: Salsa logging
Salsa User Manual 30
Scans executed actions via SalsaAPI historic (historic file)
  ds_simpleScan, passerelle and Salsa.
  Replay (exactly) a scan via Play button
  Click on the nexus file name to open it a nexus file browser application

## Slide 31: Perspectives
Salsa User Manual 31
A perspective is a windows disposition preference.
Create a perspective:
  Menu Perspective -> New
  Enter a perspective Name
Load a perspective:
  Menu Perspective -> Check the desired perspective to load.
Save a prespective:
  Hide and show the desired views (Window menu)
  Organize your views disposition
  Click on Save button
  The perspective is also saved at the software exit.
Remove a perspective:
  Menu Perspective -> Remove

## Slide 32: Data Fitter views
Salsa User Manual 32
DataFitter integration in the scan chart result
  LINE/EX/FIT.1/fittedDataY
  LINE/EX/FIT.1/deviceAttributeNameX
  LINE/EX/FIT.1/deviceAttributeNameY
data fitter attributes

## Slide 33: Data recorder views
Salsa User Manual 33
Data recording service
  LINE/EX/FIT.1/recorderData
Default configuration of data recording service
  Menu Edit -> Preferences -> Devices
  Set true or false
Enable/Disable recording service
  Click on the Data recorder button
data recorder attribute

## Slide 34: Bookmarks
Salsa User Manual 34
Bookmarks management
  Create a bookmark
  Fill the bookmark
  Enter a simple name for the added configuration

## Slide 35: Bookmarks
Salsa User Manual 35
Configuration selection via bookmarks
salsa-ro arguments
  salsa-ro with no argument will display 2 combo boxes: The Bookmarks list and the configuration list associated to a selected bookmark
  salsa-ro bookmark_name (salsa-ro NewList2) will display 1 combo box: The configuration list associated to the bookmark named in argument
  salsa-ro configuration_name (salsa-ro root/Katy/My1DConfig) will display the view with directly the configuration named in argument.

## Slide 36: Salsa search tool
Salsa User Manual 36
In order to quickly find a configuration
  Type a text to find in a configuration name
  Click on Next (>>) button or Previous (<<) button to find all matching configurations

## Slide 37: Custom Trajectory
Salsa User Manual 37
Trajectory Y
Trajectory X
Trajectory Editor
Trajectory Menu

## Slide 38: Salsa open Nexus files
Salsa User Manual 38
Open a nexus file in the databrowser
  Click on a nexus file name to open it in the databrowser.

## Slide 39: Get trajectory from scan image
Salsa User Manual 39
Declare a Publisher device in Tango database:
  Device Server name: Publisher/SAV-SCAN-TRAJ
  Device name: tango/CA/PubScanTraj.1
  Properties:
Configure Salsa to access to Export Trajectory option:
  To get the expected menu in Salsa, more precisely in the « Image » tab of the « Scan Result » tab, you have to declare the publisher that will receive the trajectory.
  Menu Edit -> Preferences, select Devices and fill Publisher field with tango/CA/PubScanTraj.1
  The following Export Trajectory button will be available:

## Slide 40: Get trajectory from scan image
Salsa User Manual 40
Select points in scan image:
  Right click on image -> Selection mode
  Either select n points on image with « Point ROI Mode » tool,
  Or select a line on image with « Line ROI Mode » tool,
  Or go back to default cursor with « Selection Mode » tool.
Remove points:
  Right click on image -> Selection mode -> « Delete all Rois » red cross

## Slide 41: Get trajectory from scan image
Salsa User Manual 41
Save trajectory:
  First, choose « X actuator » and « Y actuator » in image tab.
  Click on « Export Trajectory » button
  If a line was chosen, then a step number should be fulfilled.
  The trajectory content (n X,Y couples) will have to be obtained from the trajectory Spectrum attribute of the Publisher device. (cf. tango/CA/PubScanTraj.1/trajectory)
Trajectory extraction:
  Example of 5 points
  extraction from python: